## Slide 1
Multimedia SoC Design
Jan. 22, 2021
Presenter: Tang Lee, I-Ting Lin, Cheng-Yan Du
Graduate Institute of Electronics Engineering, National Taiwan University
Feature-Based Image Morphing Accelerator on PYNQ
Github: https://github.com/MRdudu156/MSOC_2020_FINAL_Project_group7/tree/main

## Slide 2: Outline
Introduction
Algorithm
System Architecture
Kernel Optimization with Vivado HLS
Implementation Result
Summary

## Slide 3: Outline
Introduction
  Feature-based Image Morphing
Algorithm
System architecture
Kernel Optimization with Vivado HLS
Implementation Result
Summary

## Slide 4: Introduction
Image morphing is a special effect in motion pictures or animations
  Changes one image into another through a seamless transition
Source image
Destination image
Target image

## Slide 5: Introduction
Widely used in animations, advertisements or movies
  Lots of Apps provide morphing special effects

## Slide 6: About The Project
This final project contains:
  Software (Python & MATLAB) implementation of image morphing algorithm
    For hardware verification
    Integrated with host program run on PYNQ platform
  Hardware implementation
    Implement the image morphing algorithm in C++
    Synthesized by Xilinx’s High-Level Synthesis (HLS) tool
    The whole system is built by Xilinx’s Vivado design suite and run on PYNQ platform in Zedboard

## Slide 7: Outline
Introduction
Algorithm
System Architecture
Kernel Optimization with Vivado HLS
Implementation Result
Summary

## Slide 8: Algorithm
Feature-based image morphing consists of two steps
  Pre-warp the two images
    Align features that appear in both images
    Reposition all pixels in the source & destination images
  Cross-dissolve their color
    A weighted combination of two images, pixel-by-pixel
Requires lots of computation

## Slide 9: Warping (1/2)
Beier-Neely algorithm
  Feature-based morphing
Specify feature line-segment
Destination image
Target image
Source image
Linear line-segment interpolation Lt

## Slide 10: Warping (2/2)
After warping, relative position of each pixel & feature lines in target image remains the same as in source image
Source image
Target image
Mapping function

## Slide 11: Blending
Linearly interpolate the warped source & warped destination images
Warped image 1
Warped image 2
Morphed result

## Slide 12: Algorithm Flow
Image size: 256x256
Feature line number: 8
Total complexity (32float operation)
  23.9M FLOP
  11.1M additions
  7.99M multiplications
  2.10M divisions
  2.62M square root
Iterate
LineNum times
Iterate for 65536 pixels
Notes: FLOPs: normalize to multiplication
Add = 0.5 mul
Mul = 1 mul
Div = 6 mul
Sqrt = 12.5 mul
The total complexity is for one image

## Slide 13: Outline
Introduction
Algorithm
System Architecture
Kernel Optimization with Vivado HLS
Implementation Result
Summary

## Slide 14: System Flow
Create feature line
Blending
Output GIF
Image morphing
Return image map
Control signal
Line info
image map
Kernel
Host
Host

## Slide 15: System Block Diagram
Zedboard@100MHz
Input and output data interface: AXI4
Control register interface: AXI4-Lite
Data width is 32 bit

## Slide 16: I/O Interface
Line information
Control signal
Output image map
AXI for I/O data
AXI-Lite for control signal

## Slide 17: I/O Packing
Pack data together to make full use of bus bandwidth
One coordinate should be represented by two uint8 numbers
Line segment information
  Wrap the two endpoint coordinates together
  Point: 32-bit unsigned integer
  Length: 32-bit float
Morphed image map
  Wrap source coordinates with dst coordinates
  Point: 32-bit unsigned integer

## Slide 18: I/O Packing

## Slide 19: I/O Packing

## Slide 20: Outline
Introduction
Algorithm
System Architecture
Kernel Optimization with Vivado HLS
Implementation Result
Summary

## Slide 21: Kernel Optimization
Four versions of kernel implementation
  Solution 1: Floating-point representation
  Solution 2: Pipeline pragma
  Solution 3: Fixed-point representation
  Solution 4: Look-up table division

## Slide 22: Solution 1: Floating-point Representation
All vectors and lengths are represented by 32-bit FP.
  Floating-point adders, multipliers, dividers, and fsqrt are synthesized.
  Target clock period is set to 10.00 ns.
  Total latency is about 188 ms.

## Slide 23: Solution 2: Pipeline Pragma
Add PIPELINE pragma to the innermost feature line loop, and use INLINE pragma to make sub-functions under the effect of PIPELINE.
  Different feature lines can be processed at the same time.
  Latency is reduced from 188 ms to 90 ms (52% reduction).
II=5

## Slide 24: Solution 2: Pipeline Pragma
Initiation interval is limited by 5-cycle floating-point addition.
Timing doesn’t meet the target clock period.

## Slide 25: Solution 3: Fixed-point Representation
All vectors and lengths are represented by 24 bit-width fxp with 10 integer bits.
HLS arbitrary precision data type: ap_fixed<W,IW>
Some operations need to be replaced with fixed-point version.
  Cordic_sqrt: calculate magnitude for distance and weight
  Fxp_sqrt: calculate square root for weight
0 | 1 | …… | 1 | 1 | 0 | 1 | …… | 1 | 0
Integer (10-bits)
Fraction (14-bits)

## Slide 26: Solution 3: Fixed-point Representation
Cordic_sqrt (source: https://github.com/Xilinx/HLx_Examples)
We adopt CORDIC vector mode for computing magnitude.
  Replace rotation multiplications with simple shift-and-add operation.
  Iteratively rotates the initial vector (x, y) to x-axis.
Scaling factor
Decision by the sign of y
Pseudo-rotations

## Slide 27: Solution 3: Fixed-point Representation
Fxp_sqrt (source: ~Xilinx/Vivado/2019.2/examples/design)
Non-restoring square root algorithm
  The square root is generated digit-by-digit.
01 01 11 01 . 00
- 1
00 01
- 1 01
11 00 11
+10 11
11 11 10 01
+ 1 00 11
1 00 00 11 00
1 0 0 1 .
Positive partial remainder
Square root result
q = (q3, q2, q1, q0)
Subtract (q(1) 01)
q(1) = 1
q(2) = 10
q(3) = 100
q(4) = 1001
Negative partial remainder
Add (q(2) 11)
q3 = 1
q2 = 0
q1 = 0
q0 = 1
Negative partial remainder
Add (q(3) 11)
Overflow
Guess q3 = 1
Square root digit
Notes: Dividend每次均用兩個bit檢查

## Slide 28: Solution 3: Fixed-point Representation
Fxp_sqrt (source: ~Xilinx/Vivado/2019.2/examples/design)
Non-restoring square root algorithm
  The iteration process can be pipelined.
Positive partial remainder, Subtract (q(i) 01)
Negative partial remainder, Add (q(i) 11)

## Slide 29: Solution 3: Fixed-point Representation
We test the accuracy by c-sim and compare with the result of floating-point version.
From the coordinate displacement histogram, we can find that most of the pixels displace from the correct coordinates by 1 to 3 pixels.
Small displacements won’t affect the morphed result too much.
Most of the displacements are small enough

## Slide 30: Solution 3: Fixed-point Representation
All vectors and lengths are represented by 24 bit-width fxp with 10 integer bits.
  With pipelining, the latency is about 303 ms (worse than solution 1).
  Initiation interval becomes too large.
  The LUT resource requirement is unaffordable.
II=139
LUT resource is overflow

## Slide 31: Solution 3: Fixed-point Representation
Fixed-point division is the bottleneck
  About 80 cycles are required
  Consume most of the resource
The cost of direct division is too high.

## Slide 32: Solution 4: Look-up Table Division
Replace the division operations with look-up table
  Division by distance/length of feature lines
  Division by weight
MATLAB simulation shows the distribution histogram.
  The suitable range and precision of LUT can be decided.
Distance distributes over (0, 256)
Weight distributes over (0, 80)
Most of the weights are small values
=> Higher precision requirement

## Slide 33: Solution 4: Look-up Table Division
The division is replaced by multiplication with the reciprocal of denominator.
Precision requirement
  Division by distance/length of feature lines: range(0,29) with precision 2(-3)
  Division by weight: range(0,26) with precision 2(-6)
Distance LUT | 
4 | 0.250
8 | 0.125
Feature line length
Distance from pixel to feature line
Numerator x
Result = x/y
Weight LUT | 
2.0 | 0.500
2.5 | 0.400
Weight
Numerator x
Result = x/y
1/y
y

## Slide 34: Solution 4: Look-up Table Division
Replace the division operations with look-up table
  Latency is significantly reduced to 14.4 ms.
  Resource requirement is greatly reduced.
  LUT is implemented using BRAM on board.
II=1
BRAM for look-up table

## Slide 35: Selected Mirco-Architecture
Solution 4 (fxp with LUT division) achieves the shortest latency with affordable hardware resource.
Thus, we adopt solution 4 for further implementation on board.
 |  | Solution 1 | Solution 2 | Solution 3 | Solution 4
Latency (ms) |  | 188.0 | 90.0 | 303.0 | 14.4
Resource (%) | LUT | 35 | 33 | 102 | 20
 | FF | 12 | 13 | 52 | 5
 | DSP48E | 14 | 12 | 16 | 29
 | BRAM_18K | 0 | 0 | 0 | 6

## Slide 36: Outline
Introduction
Algorithm
System Architecture
Kernel Optimization with Vivado HLS
Implementation Result
Summary

## Slide 37: Comparison
Compare our design with CPU: Intel i7-6700 @3.4GHz
Image size = 256x256
Number of feature lines = 8
Task: generate a sequence of morphed images (total 11 images)
 | Our system (PYNQ + Zedboard) | CPU (Python program)
Operating frequency (Hz) | 100M (kernel) | 3.4G
Latency (s) | 1.29 | 406
Throughput (morphed img./s) | 8.5 | 0.03
315x speed up!

## Slide 38: Demo

## Slide 39: Demo

## Slide 40: Outline
Introduction
Algorithm
System Architecture
Kernel Optimization with Vivado HLS
Implementation Result
Summary

## Slide 41: Summary
Feature-based image morphing is introduced
  A special effect widely used in animations, movies, etc.
Image morphing consists of two major steps: Warping and Blending
  Warping requires lots complex computation such as square root and division
  Warping allows pixel-level parallelism which is suitable for hardware acceleration
An optimized micro-architecture of kernel function is designed under several analysis
  24-bit fixed-point datatype
  CORDIC for magnitude computation & Non-restoring square-root algorithm
  Division is replaced by LUT
Implementation result is compared with Python program run in Intel i7-6700 CPU
  315x speed up for generating a morphed images sequence

## Slide 42: Reference
[1] Feng Zhu, “Image Morphing with the Beier-Neely Method,” B.Sc., Northwestern Polytechnical University, 2013.
[2] https://www.xilinx.com/support/documentation/sw_manuals/xilinx2018_3/ug902-vivado-high-level-synthesis.pdf
[3] T. Sutikno, “An efﬁcient implementation of the non restoring square root algorithm in gate level,” technology, vol. 1, no. 3, pp. 5–10, 2011.