## Slide 1: Final Presentation
Heston Implementation for Zynq with Vivado HLS
Group 14: 陳柏帆 張問寬

## Slide 2: Outline
Project Introduction
  Motivation
  Random Number Generator
  Heston Model
System Introduction
  Code Base
  Block Diagram
  Target Performance
  Computation Complexity
μ-archi. & Optimization
  Mersenne Twister
  ICDF
  Heston
Implementation on Zynq

## Slide 3: Outline
Introduction to the system
  Motivation
  Random Number Generator
  Heston Model
  Block Diagram
Optimization
  Mersenne Twister
  ICDF
  Heston
Implementation on Zynq

## Slide 4: Project Introduction

## Slide 5: Motivation
To determine the pricing of an option, financial institutes need to estimate the price of the asset after a certain period.
Several mathematical models are presented, but few have closed form solutions.
Numerical methods are more common but computationally expensive. This work aims to accelerate the computation of the numerical solution of Heston model.

## Slide 6: Random number generator
Normal distribution is preferred, but uniform distribution is easier to generate, i.e. Mersenne twister.
Use the inverse CDF to map uniform distribution to normal distribution.
In practice, inverse CDF is divided into segments, and we use polynomial to approximate each segment.

## Slide 7: Heston model
In finance, the Heston model, named after Steven Heston, is a mathematical model describing the evolution of the volatility of an underlying asset.
It is a stochastic volatility model: such a model assumes that the volatility of the asset is not constant, nor even deterministic, but follows a random process.

## Slide 8: Heston model - terminologies
r : interest rate of an risk-free asset
St: price of the asset at time t
dt: interval between each step
vt: volitility, describes how drastic the price fluctuates
W: a random process

## Slide 9: Heston model - terminologies
θ: long term average volitlity
K:reversion rate, how fast the volatility move towards theta
ξ:volitility of volitility, describes how drastic the volitility fluctuates

## Slide 10: Heston model - implementation
After repeating (1) and (2) for a given step count, we have the final price of the asset for 1 simulation path.
The price we have, however, is not accurate, for the RNG differs each time. We need multiple simulation paths to get an average price close to the answer.
Different simulations are not correlated, and thus FPGA can be used to do multiple simulations at the same time.

## Slide 11: System Introduction

## Slide 12: System Introduction
HLS code from tukl-msd/finance.zynqpricer.hls
system flow (SW/HW Partition)
SW(Pynq)
HW(Heston Engine)
Mersenne Twister
ICDF
Antithetic
Heston
Argument
Passing
Price Output Receiving

## Slide 13: Block Diagram of the System
Supports up to 6 engines.

## Slide 14: Spec & Complexity
Spec
  1.04e+07 steps/seconds, CPU computation
  5.78e+08 steps/seconds ≌ 6 engines*100MHz, FPGA accelerated
Computation Complexity
O(simulation_count * step_count_per_simulation)

## Slide 15: System Introduction - Summery
Mersenne twister and ICDF generate a gaussian random number
Antithetic adds in a negative version of each input random number, and thus doubles the data rate. This helps the simulation to converge faster.
Using the generated random numbers, heston module estimates the final price.
Parameters are initialized through axilite.
Each engine does 10000 simulations and returns 10000 final prices through AXI stream.
Use multiple engines to do parellel computation.

## Slide 17: µ-archi. & Optimization

## Slide 18: µ-archi.
Purposed of Pragma used
  System Level: Non-blocing Access
  Module Level: Mersenne Twister
  Module Level: ICDF
  Module Level: Heston
Analyze
  Scheduling of buffer transfer, kernel execution
  throughput

## Slide 19: Key Design: Non-Blocking Access
Four modules can operate at the same time. The idea is similar to dataflow between functions, but between ip blocks. Blocking access like AXIS or AXI master are not suitable.
Ap_fifo enables non-blocking access. RNG can output numbers to fifo, and Heston module can retrieve data from fifo without communication through any protocols.
  Antithetic doubles the data rate, fifo should be full the whole time, so empty is not an issue.
  The order of RNs does not matter. Excessive numbers can be dropped, so full is also not an issue.

## Slide 20: Mersenne Twister
Use two 1D arrays to store intermediate products.
Arrays are accessed sequentially. In each iteration, only one element from each array is used.
Set loop dependency=False to enable more efficient pipeline, although the improvement is minor.

## Slide 21: ICDF
Using 2 ap_fixed to represent coeff
Requires 5 BRAM to accomodate them

## Slide 22: ICDF
Read Port of BRAM is 72 bit
Using DATA_PACK to pack them into the same BRAM line
Reduced BRAM by 20%

## Slide 23: Heston
DSP Util. keeps us from adding one more engine

## Slide 24: Heston
DSP Util. keeps us from adding one more engine

## Slide 25: Heston
Analyze DSP Usage in Heston
  Floating Point Add/Sub takes 2 DSP
  Floating Point Mul takes 3 DSP

## Slide 26: Heston
Analyze DSP Usage in Heston
  Manipulate Directives to specify not to use DSP
  Reduced by 8.6%

## Slide 27: Heston
Analyze DSP Usage in Heston
  DSP Util. Reduced by 8.6%
  However, once LUT Utll. > 90%, congestion will happen
  Still not enough to add one more engine

## Slide 28: A “crippled” version of Heston engine
Loosen II limitation can significantly reduce resource usage.

## Slide 29: A “crippled” version of Heston engine
Setting II=2 can significantly reduce resource usage.

## Slide 30: A “crippled” version of Heston engine
33*6+19=217 DSP
Implemented on Pynq

## Slide 31: Improvement
Original implementation:
  (2560000 steps_per_trigger * 6 eng_triggers)/0.0266 seconds=5.78e+08 steps/seconds
Improved implementation:
  (2560000 steps_per_trigger * 13 eng_triggers)/0.0531 seconds=6.26e+08 steps/seconds
8.3% performance improvement

## Slide 32: Analysis
Scheduling (Before)
Throughput
  (10000 simulations_per_trigger * 6 triggers) / 0.0266 seconds
=2.26e+06 simulations/sec
Host(SW)
normal_eng
initialize all engs
retrieve data from normal engs
compute

## Slide 33: Analysis
Scheduling (After)
Throughput
  (10000 simulations_per_trigger * 13 triggers) / 0.0531 seconds
=2.45e+06 simulations/sec
Host(SW)
normal_eng
crippled_eng
initialize all engs
retrieve data from normal engs
re-trigger normal engs
retrieve data from all engs
compute
compute
compute

## Slide 34: Thanks for Listening!