## Slide 1: MSOC Final Project
High level synthesis for Image Deblurring Processor
Team 2
2021 01/22
r09943005 楊智翔 r09943021 舒泓諭 r09943113 董濟昀
Github: https://github.com/2020MSOC_Final

## Slide 2: Outline
Motivation High-Quality Computational Imaging Through Simple Lenses [2013]
Algorithm Primal-Dual algorithm
Hardware architecture FFT module and matrix convolution
HLS Implementation Optimization for utilization and latency
Interface
Implement on FPGA
Conclusion

## Slide 3: Motivation
Chromatic aberration is a long-existing issue in camera imaging technology. Due to the refraction difference of different colors of light, dispersion is inevitable through a single convex lens.

## Slide 4: Motivation
High-Quality Computational Imaging Through Simple Lenses [2013] proposes solution to deblurring image.
For 256x256 image,original algorithm of 50 iteration takes 0.8222 second in matlab simulation. For larger image resolution(1920x1680), it couldn’t reach real time processing latency.

## Slide 5: Goal
First HLS work for primal-dual for image deblurring
Real time image deblurring processor in Pynq-Z2

## Slide 6: System flow
HLS implement

## Slide 7: System block diagram
Image deblurring processing unit implemented in pynq-Z2

## Slide 8: Image pocessing pipeline --- Deconvolution

## Slide 9: Objective function
Data term
Regulization term
TV norm
cross channel prior
Cross-channel prior enforces gradient consistency between the color channels.
blur kernel
Reconstruction goal
blurred image

## Slide 10: Algorithm
•Antonin Chambolle, Thomas Pock [2011]:
iteratively update primal variable and dual variable
primal step
dual step
over-relaxation step

## Slide 11: Hardware for deblur
implement 2D FFT for invertible matrix
operation in dual step
implement matrix operation

## Slide 12: Proximal operator unit

## Slide 13: 2D FFT unit
Precision
Image domain 8 bit(0~255)
FFT domain 32 bit single precision(Real part /Imag part)
Xilinx logicCore IP Product library
128 point 1D FFT unit
Streaming architecture(Radix-2 butterfly)
Ref: pg109 LogiCORE IP Product Guide(Xilinx 2019)

## Slide 14: 2D FFT unit
Xilinx logicCore IP Product library four types
 | Cycle number | DSP | BRAM
Radix-4, Burst I/O | 61596 | 20 | 50
Radix-2, Burst I/O | 177679 | 6 | 36
Radix-2, Lite I/O | 262183 | 3 | 38
Pipelined Stream | 32917 | 60 | 43
Resource v.s.Throughput

## Slide 15: Xilinx IP usage
It’s very user friendly, and there’re two steps:
Define FFT parameter(ex: Precision, FFT length , Rounding type)

## Slide 16: Xilinx IP usage
(b) Handle FFT I/O buffer ,and call fft function
1D 128
FFT unit

## Slide 17: Streaming architecture (Radix-2 butterfly)
Each processing engine has its own memory banks
Pipelined architecture : simultaneously perform transform calculations on the current frame of data, load input data for the next frame of data

## Slide 18: HLS optimization for 2D FFT unit
Long latency for 2D FFT unit
Timeline analysis for resource viewer

## Slide 19: HLS optimization for 2D FFT unit
Shorter latency for 2D FFT unit
Timeline analysis for resource viewer

## Slide 20: Deblurring unit

## Slide 21
2D convolution with line buffer
Output
#pragma HLS ARRAY_PARTITION variable=line_buffer complete dim=1

## Slide 22
Brute force v.s. line buffer

## Slide 23: C code direct mapping

## Slide 24: The difference of coding methodology between Software (C++) and Hardware (HLS)
d = a + b
e = d + c
e = a +b + c
C++
HLS

## Slide 25: Preliminary HLS optimization

## Slide 26: Utilization problems in iteration algorithm
Primal-dual algorithm is an iteration-based algorithm , many dual variables needs to be saved in BRAM. Furthermore, in order to preserve accuracy in dual variables , we use floating point data type, causing utilization problem. Thus we use DDR memory.

## Slide 27: Interface
hls::stream< ap_axiu<32,1,1,1>>
  Instream
  outstream
s_axilite
  Return
  block level protocol indicate data on function port is valid and can be read

## Slide 28: Data packing
decrease latency
decrease cycles used by axi stream
stream for R
need 128*128 cycles
stream for G
need 128*128 cycles
stream for B
need 128*128 cycles
total 3*128*128 cycles
ap_axiu<32,1,1,1> indata
indata( 7, 0) = R
indata(15, 8) = G
indata(23,16) = B
total 128*128 cycles

## Slide 29: Block Diagram for AXI stream

## Slide 30: DDR memory
axi master burst
memcpy function
burst write of WIDTH ints from Ram to DDR

## Slide 31: DDR memory
need to think about hardware usage
only register variables when needed
software coding style,
need 4 integer
hardware coding style, with memory reusing
only 2 integer

## Slide 32: HLS Synthesize
Arrays in the C code synthesize into block RAM or UltraRAM in the final FPGA design
If the array is on the top-level function interface, high-level synthesis implements the array as ports to access a block RAM outside the design.
block level follow C++ memory assign logic

## Slide 33: HLS Synthesize
array at top level
array in block level

## Slide 34: HLS Synthesize
same function, but different BRAM usage
array at top level
array in block level

## Slide 35: Conclusion
First high level synthesis for image deblurring for primal dual algorithm
FPGA interface for delivering data
Github submit ：https://github.com/leo870823/2020MSOC_Final

## Slide 36: Reference
An Image Deblurring Processor for Chromatic Aberration Based on the Primal-Dual Algorithm with Cross-Channel Prior (Chia-Han Huang,[2020 ISCAS])
High-Quality Computational Imaging Through Simple Lenses(Felix Heide,[2013])
A first-order primal-dual algorithm for convex problems with applications to imaging(Antonin Chambolle, Thomas Pock [2011])
HLS IP Library https://cloud.tencent.com/developer/article/1605517

## Slide 37: Thank you for your attention