## Slide 1: Image Stitching System Based on ORB Feature
Team 13
GITHUB LINK:
https://github.com/RitaWen/Image-Stitching-System-Based-on-ORB-feature

## Slide 2: Outline
Image Stitching
Workflow and Algorithm
System Architecture and Spec
Design Optimization
Result

## Slide 3: Image Stitching
Combine multiple images and create a panorama

## Slide 4: Workflow
Keypoints extraction
Feature description
Feature matching
Cylindrical projection
RANSAC
Image blending
ORB
(Oriented FAST and rotated BRIEF)
Eliminate outliers
Determine relative positions of input images

## Slide 5: Cylindrical projection

## Slide 6: Keypoints extraction: FAST
Detect corners
  P is a candidate if there are n consecutive all > P0+threshold or all < P0-threshold
  Scoring: find V s.t. exactly n consecutive points all > P0+threshold or all < P0-threshold
  n = 12

## Slide 7: Keypoints extraction: FAST
NMS (non-maximum suppression)
  Remove redundant points
  Only keep one point with highest score in a 9x9 window

## Slide 8: Feature description: BRIEF
Orientation:
  Vector from a corner’s center to moment
BRIEF descriptor:
  Binary test between two points in a patch
  Test pairs N=256
rBRIEF:
  Rotate binary tests
x
y
Patch 31x31
Gaussian distribution
N = 256
V=[0 1 0 1 1 1 0 0…]
256 bits

## Slide 9: Feature matching
Hamming distance between two 256 bits descriptor
For each corner in fig1, find corners in fig2 with 1st and 2nd distance
Match: (1st dist / 2nd dist) < 0.5
Total n1*n2 times
  #corners in fig1: n1
  #corners in fig2: n2

## Slide 10: RANSAC
Eliminate outliers
Poll for best relative displacement:
Determine the offset and related position between images

## Slide 11: Image blending

## Slide 12: Software implementation
Run on intel i7-10700 CPU @ 3.80GHz with MATLAB
Run time: 9 images of size 450x278
 | Run time (s) | Throughput (pixel/s)
Cylindrical projection | 2.380 | -
ORB | 45.784 | 2732.40
Feature matching | 57.355 | 160,000~640,000 (500~1000 corners)
RANSAC | 0.0110 | -
Blending | 3.351 | -
Total time | 110.061 | -
Bottleneck
Need to reduce run time and increase throughput!!

## Slide 13: Target Spec
Speed-up: 10x
Target throughput:
 | intel i7-10700 CPU | Target
ORB | 2732 pixel/s | 27324 pixel/s
Feature matching | 160,000~640,000 pair/s | 1,000,000 pair/s
Achieve higher throughput and lower latency

## Slide 14: System Architecture
ORB
Kernel
Matching
Kernel
Cylindrical
Projection
RANSAC
Blending
Img_cyl
feature
Match_pt
PS
PL
Input
image
Output image

## Slide 15: ORB Kernel
FAST
NMS
Moment
Gaussian
Filter
Descriptor
Input
image
Output
Corners/descriptors
Ref: https://github.com/Siudya/ORB_FPGA?fbclid=IwAR3j4uoTPw_2FZh24xS1qVgnz4C3wclwXm9ZgUTw7_qJV7wVTXbjUrBJzDY
8’
32’
[D1, D2….D10, X, Y]
32 bits integer*10

## Slide 16: ORB Kernel - Optimization
Bottleneck: Descriptor (~83% run time of ORB)
If-else condition in for loop
Unroll

## Slide 17: ORB Kernel - Optimization
Original
Unroll
Much shorter runtime, but insufficient resources…?

## Slide 18: ORB Kernel
Clock Frequency: 160MHz
Actual Utilization:
HLS report is not accurate!!!
Vivado tool will optimize in APR.

## Slide 19: ORB Kernel - Optimization
Larger window in NMS
Reduce corners -> Faster in calculate descriptor and feature matching
  3 x 3: ~2000 keypoints/image
  9 x 9: ~600 keypoints/image
Almost no degradation in quality (verified in software)

## Slide 20: Matching Kernel
Hardware Implementation
Hamming
distance
1st / 2nd
comparator
1st / 2nd
dist
Input
Corners/descriptors
Output
Matched points
32’
32’
[X1Y1, X2Y2]
(16, 16) bits integer*2

## Slide 21: Matching Kernel - Optimization
Loop Unrolling (factor=256)
Compare multiple pairs concurrently
~5x faster compared to software implementation !!

## Slide 22: Result
BL430: 3 images with size 739x526

## Slide 23: Result
Office: 3 images with size 534x756

## Slide 24: Result
傅鐘: 9 images of size 450x278

## Slide 25: Runtime after acceleration
9 images of size 450x278
Run time
Throughput
 | Intel i7 CPU | Zedboard
ORB | 45.784 (s) | 0.083 (s)
Feature matching | 57.355 (s) | 13.2 (s)
 | Intel i7 CPU | Zedboard
ORB | 2732 pixel/s | 1,507,229 pixel/s
Feature matching | 160,000~640,000 pair/s | 681,818~2,727,272 pair/s
~550x
~4x