## Slide 1: Real-time 3D Rendering
Team 04
https://github.com/victoresque/HLS3D

## Slide 2: Outline
Introduction
Algorithm Overview
Kernel Implementation
Design Optimization
System Integration
References

## Slide 3: Introduction to 3D Rendering
Rendering: visualizing 3D objects and scenes
Applications
  Real-time: video games, AR, …
  Non real-time: movie, interior design, …
High computational complexity

## Slide 4: Outline
Introduction
Algorithm Overview
Kernel Implementation
Design Optimization
System Integration
References

## Slide 5: 3D Object Representation
3D objects consist of vertices and faces/triangles
Each vertex contains these information:
  Coordinates
  Texture coordinates
  Face norm vector
  … and more

## Slide 6: Rendering Process
Geometric transform
Visibility checking
Rasterization and interpolation
Texture mapping
Shadow mapping
Blending

## Slide 7: Geometric Transform
3D models are stored in object local coordinates
Moving an object around in a scene
  from local coordinates to world coordinates
To simplify rendering computation
  transform to camera coordinates
source: http://ycpcs.github.io/cs470-fall2014/labs/lab07-2.html

## Slide 8: Visibility Checking
If two points projects to the same pixel, the closer one is visible
Use a depth buffer to track minimum distance per pixel
for point in scene:
pixel <- project(point)
if point.z < depth_buffer[pixel]:
depth_buffer[pixel] = point.z
// rasterization
camera
projection
plane
p1
p2
q1
q2
p'
q'
z

## Slide 9: Interpolation (1/2)
Interpolation should consider perspective for correct results
naïve
perspective-corrected

## Slide 10: Interpolation (2/2)
Interpolation should consider perspective for correct results
Naïve:
Perspective-corrected:
naïve
perspective-corrected
A
P1
P2
P3
A1
A2
A3

## Slide 11: Smooth Shading
Interpolate vertex normals to smooth out edges
source: https://www.scratchapixel.com/lessons/3d-basic-rendering/introduction-to-shading/shading-normals
with smooth shading
without smooth shading

## Slide 12: Software Implementation (1/3)
We implemented the rasterization-based rendering in Python before implementing hardware kernel with C++/HLS
Performance
  640x480, ~0.2fps on Intel Core i7 @3GHz

## Slide 13: Software Implementation (2/3)
Example scene 1: cast shadow, no texture, no smooth shading
Example Scene 2: texture mapping, smooth shading
shadow map
shadow
render result

## Slide 14: Software Implementation (3/3)
Comparison: smooth shading
with smooth shading
without smooth shading

## Slide 15: Outline
Introduction
Algorithm Overview
Kernel Implementation
Design Optimization
System Integration
References

## Slide 16: Kernel Interface Design (1/2)
64-bit AXI4-Stream for data input and output
  2 floats per cycle
Each face is represented by 24 floats
  3 vertices per face
    3 coordinates (x, y, z)
    3 normal vector (nx, ny, nz)
    2 texture coordinates (tx, ty)
  12 cycles per face

## Slide 17: Kernel Interface Design (2/2)
Register map
Offset | Name | Description
0x00 | ap_control | Kernel start/done/idle/ready signals
0x10 | mode | Operating mode (0: reset, 1: texture, 2: mesh in, 3: frame out, 4: transform)
0x18 | num_faces | Number of faces
0x80 | obj_scale | Geometric transform object scale
0x88 | texture_id | Texture ID
0x40~0x7f | transform | Geometric transform matrix (3x4)
0x90~0x9f | lnorm | Light direction vector
0xa0~0xaf | cam_scale | Camera projection scale
0xb0~0xbf | cam_offset | Camera projection offset
0xc0~0xc7 | frameh | Frame height range

## Slide 18: Kernel Operating Modes
Mode 0: reset
  Reset frame buffer, depth buffer, and texture buffer
Mode 1: load texture
  Load texture data (up to four textures)
  Input: 2 RGBX pixels per cycle, total 64x64 pixels
Mode 2: mesh stream in and rasterize
  Load face data and render a tile of frame
  2 floats per cycle, total 24 floats per face
  Input: (tx0, ty0), (nx0, ny0), (nz0, vx0), (vy0, vz0), (tx0, ty1), …

## Slide 19: Kernel Operating Modes (2/2)
Mode 3: frame out
  Store frame buffer to DRAM
  Output: 2 RGBX pixels per cycle
Mode 4: geometric transform
  Transform mesh data using a transform matrix
  Input: 24-float face data (t, n, v)
  Output: transformed 24-float face data (ct, cn, cv)

## Slide 20: Implementing Geometric Transform
Geometric transform is performed once per frame
for (int i = 0; i < num_faces; i++) {
#pragma HLS pipeline II=12
apuint64_1_to_half_2(stream_input->read().data, t0[0], t0[1]);
// ... stream in 24 floats for each face
apuint64_1_to_half_2(stream_input->read().data, v2[1], v2[2]);
matrix_mul_vector(0, transform_h, obj_scale, v0, cv0);
matrix_mul_vector(0, transform_h, obj_scale, v1, cv1);
matrix_mul_vector(0, transform_h, obj_scale, v2, cv2); matrix_mul_vector(1, transform_h, 1.0, n0, cn0);
matrix_mul_vector(1, transform_h, 1.0, n1, cn1);
matrix_mul_vector(1, transform_h, 1.0, n2, cn2);
ct0[0] = t0[0]; ct0[1] = t0[1];
ct1[0] = t1[0]; ct1[1] = t1[1];
ct2[0] = t2[0]; ct2[1] = t2[1];
float_2_to_apuint64_1(ct0[0], ct0[1], stream_data.data);
stream_output->write(stream_data);
// ... stream out 24 floats for each face
float_2_to_apuint64_1(cv2[1], cv2[2], stream_data.data);
stream_output->write(stream_data);
}

## Slide 21: Implementing Rasterization (1/2)
for (int i = 0; i < num_faces; i++) {
#pragma HLS pipeline II=12
apuint64_1_to_half_2(stream_input->read().data, ct0[0], ct0[1]);
// ... stream in 24 floats for each face
apuint64_1_to_half_2(stream_input->read().data, cv2[1], cv2[2]);
l0 = lambt+vector_dot_vector(cn0, lnormh)*(1.0-lambt);
l1 = lambt+vector_dot_vector(cn1, lnormh)*(1.0-lambt);
l2 = lambt+vector_dot_vector(cn2, lnormh)*(1.0-lambt);
cam_project(cv0, cam_scale, cam_offset, fv0, fv0i);
cam_project(cv1, cam_scale, cam_offset, fv1, fv1i);
cam_project(cv2, cam_scale, cam_offset, fv2, fv2i);
if ((fv0[2]<clip) && (fv1[2]<clip) && (fv2[2]<clip)) continue;
area = triangle_area(fv2, fv1, fv0);
if (area<=0) continue;
fz0_1 = 1/fv0[2];
fz1_1 = 1/fv1[2];
fz2_1 = 1/fv2[2];
fymax = imin(fh[1]-1, imax(fv0i[1], imax(fv1i[1], fv2i[1])));
fymin = imax( fh[0], imin(fv0i[1], imin(fv1i[1], fv2i[1])));
fxmax = imin( 640-1, imax(fv0i[0], imax(fv1i[0], fv2i[0])));
fxmin = imax( 0, imin(fv0i[0], imin(fv1i[0], fv2i[0])));
(fxmin, fymin)
(fxmax, fymax)
calculate triangle bounding box
project point to frame
calculate vertex luminance

## Slide 22: Implementing Rasterization (2/2)
for (int fy = fymin; fy <= fymax; fy++) {
#pragma HLS pipeline
for (int fx = fxmin; fx <= fxmax; fx++) {
#pragma HLS pipeline
#pragma HLS dependence variable=depth_buffer inter false w0 = triangle_area(fx, fv2, fv1)/area;
w1 = triangle_area(fy, fv0, fv2)/area;
w2 = triangle_area( 1, fv1, fv0)/area;
if ((w0>=0) && (w1>=0) && (w2>=0)) {
fz_1 = w0*fz0_1+w1*fz1_1+w2*fz2_1;
fz = 1/fz_1;
if ((fz>=clip) && (fz<depth_buffer[fy-fh[0]][fx])) {
depth_buffer[fy-fh[0]][fx] = fz;
ct[0] = round(64*(w0*ct0[0]*fz0_1+w1*ct1[0]*fz1_1+w2*ct2[0]*fz2_1)*fz);
ct[1] = round(64*(w0*ct0[1]*fz0_1+w1*ct1[1]*fz1_1+w2*ct2[1]*fz2_1)*fz); lum = (w0*l0*fz0_1+w1*l1*fz1_1+w2*l2*fz2_1)*fz; frame_buffer[fy-fh[0]][fx][0] = (texture[texture_id][ct[0]][ct[1]][0])*lum;
frame_buffer[fy-fh[0]][fx][1] = (texture[texture_id][ct[0]][ct[1]][1])*lum;
frame_buffer[fy-fh[0]][fx][2] = (texture[texture_id][ct[0]][ct[1]][2])*lum;
}
}
}
}
perspective-corrected interpolation
visibility checking
iterate through pixels in the bounding box
frame buffer update
check if pixel is inside the triangle

## Slide 23: HLS Synthesis Result
Using too much BRAM resource
  Cannot be deployed to ZedBoard
High LUT usage, need to reserve some LUTs for integration

## Slide 24: Outline
Introduction
Algorithm Overview
Kernel Implementation
Design Optimization
System Integration
References

## Slide 25: Using Half-precision Floating-points (1/2)
The resource usage is too high for a 32-bit float design
  We can trade off precision for lower resource usage
Example:
  A half multiplier (dspnone): 159LUTs, 204FFs
  A float multiplier (dspnone): 567LUTs, 692FFs
  Overall 2~3x less resource
https://www.xilinx.com/support/documentation/ip_documentation/ru/floating-point.html

## Slide 26: Using Half-precision Floating-points (2/2)
Render results comparison: float vs. half
No significant difference under 640x480 resolution
float (32-bit)
half (16-bit)

## Slide 27: Tiled Frame Rendering
A 640x480 RGB frame is too large for ZedBoard BRAM
Reduce buffer to 640x60, render a frame in 8 iterations
  Face data is streamed in each iteration
  Frame buffer is streamed out after rasterizing all objects
Results:
-88%
-16%
-20%
-35%

## Slide 28: Outline
Introduction
Algorithm Overview
Kernel Implementation
Design Optimization
System Integration
References

## Slide 29: System Specifications
Platform: ZedBoard
Frequency: 250 MHz (synthesized under 100 MHz)
Video format: 640x480 (HDMI)
Frame rate: 20fps (depending on number of faces) 1200x speed up compare to Core i7, frequency normalized

## Slide 30: HDMI Output Integration (1/2)
ZedBoard uses ADV7511 as an HDMI transmitter
To integrate ADV7511 in the system:
  Use ADX_HDMI_TX IP provided by Analog Devices
  Use Xilinx AXI IIC IP to configure ADV7511
  Initialize ADX_HDMI_TX registers using PYNQ
  Initialize ADV7511 registers using PYNQ
  Use Xilinx Video Test Pattern Generator to test HDMI
  Integrate Xilinx Video Frame Buffer Read for frame reading

## Slide 31: HDMI Output Integration (2/2)
ADV7511 Programming (I2C)
ADV7511 register specs
ipIIC.send(0x39, bytes([0x41, 0x50]), 2) # power down
ipIIC.send(0x39, bytes([0x15, 0x01]), 2) # 16,20,24b YCbCr422
ipIIC.send(0x39, bytes([0x16, 0x35]), 2) # 4:4:4, 8b, style2,
ipIIC.send(0x39, bytes([0x17, 0x00]), 2) # 4:3
ipIIC.send(0x39, bytes([0x40, 0x80]), 2) # GC packet enable
ipIIC.send(0x39, bytes([0x48, 0x08]), 2) # bit right justified
ipIIC.send(0x39, bytes([0x49, 0xa8]), 2) # bit trim: truncate
ipIIC.send(0x39, bytes([0x98, 0x03]), 2) # fixed
ipIIC.send(0x39, bytes([0x9a, 0xe0]), 2) # fixed
ipIIC.send(0x39, bytes([0x9c, 0x30]), 2) # fixed
ipIIC.send(0x39, bytes([0x9d, 0x61]), 2) # fixed
ipIIC.send(0x39, bytes([0xa2, 0xa4]), 2) # fixed
ipIIC.send(0x39, bytes([0xa3, 0xa4]), 2) # fixed
ipIIC.send(0x39, bytes([0xaf, 0x06]), 2) # HDMI mode
ipIIC.send(0x39, bytes([0xe0, 0xd0]), 2) # fixed
ipIIC.send(0x39, bytes([0xf9, 0x00]), 2) # fixed
ipIIC.send(0x39, bytes([0xd6, 0xc0]), 2)
ipIIC.send(0x39, bytes([0x41, 0x10]), 2) # power up
our programming sequence in PYNQ

## Slide 32: System Block Diagram
Render kernel
OutputDMA
HDMI Controller
ZYNQ
Data Interconnect
Control Interconnect
Input DMA
I2C for ADV7511
Video Test Pattern
Generator
Frame Buffer Reader

## Slide 33: Hardware-Software Scheduling (1/4)
Use separate render kernel thread (runs on kernel) and scene control thread (runs on host CPU)
Rasterization is a pixel-wise operation
  Require hardware kernel to accelerate
Scene logic and transform matrices are object-wise operations
  Can be done by CPU in real-time
foreach frame:
render_thread.start()
// scene logic
// calculate object transform matrix
// calculate light transform matrix
// calculate camera matrix
render_thread.join()

## Slide 34: Hardware-Software Scheduling (2/4)
Use separate render kernel thread (runs on kernel) and scene control thread (runs on host CPU)
function render_thread():
for obj in objects:
kernel.transform(obj, obj.transform)
for iteration in [0,8):
kernel.set_frame_tile_range(60*(i+0),
60*(i+1))
for obj in objects:
kernel.set_num_faces(obj)
kernel.set_texture_id(obj)
kernel.rasterize(obj)
kernel.store_frame_tile(frame_buffer)
return
foreach frame:
render_thread.start()
...
render_thread.join()

## Slide 35: Hardware-Software Scheduling (3/4)
time
Video IPs init
Frame Buffer Read
Model data (DRAM)
Load model from SD card
Render kernel init
Scene
Thread
(software)
Scene logic (frame 1)
Scene logic (frame 2)
Render
Thread
(hardware)
Scene logic (frame 3)
Frame buffer (DRAM)
Frame
Buffer
(hardware)
HDMI
Frame Buffer Read
Frame Buffer Read
HDMI
HDMI
HDMI
Frame Buffer Read
HDMI
Frame Buffer Read
HDMI
Frame Buffer Read
HDMI
Frame Buffer Read
System scheduling
fork
join
fork
join
fork
Render routine (frame 2)
Render (frame 3)
Render routine (frame 1)

## Slide 36: Hardware-Software Scheduling (4/4)
Render routine (hardware)
Render
routine
time
Rasterize
Frame Tile 1
Rasterize
Frame Tile 2
…
Rasterize
Frame Tile 8
Render frame 2
Render frame 3
Render frame 4
Geo. trans
routine
Set obj1 trans
Run trans
kernel
Set objN trans
Run trans
kernel
…
Rasterize
routine
Frame Tile
range setup
Reset
buffers
Rasterize
obj1
Rasterize
objN
…
Store
frame buffer
time
Render frame1
Geometric transform

## Slide 37: Demo
Demo setup: https://youtu.be/3ftIn4NvHJQ
Close-up: https://youtu.be/YF6Qrvv0G5I
UART terminal
HDMI
output
ZedBoard
640x480
resolution

## Slide 38: References
[1] https://www.scratchapixel.com/lessons/3d-basic-rendering/rasterization-practical-implementation
[2] https://learnopengl.com/Advanced-Lighting/Shadows/Shadow-Mapping
[3] https://www.xilinx.com/support/documentation/sw_manuals/xilinx2018_3/ug902-vivado-high-level-synthesis.pdf