## Slide 1: 2020 MSoC Final Project Presentation
Team 17
Github:
https://github.com/R09943156/MSOC/tree/main/final

## Slide 2: Outline
Problem Formulation
(Discrete) Fractional Fourier Transform
Algorithm Simulation
Hardware Architecture & HLS Optimization
Bring up PYNQ System
Conclusion

## Slide 3: Problem Formulation (1/2)
We can use Fourier Transform to do the filtering in frequency domain.
However, when the time-frequency plot is shown as below, such signal can’t be filtered using Fourier Transform.

## Slide 4: Problem Formulation (2/2)
Our goal is to obtain the clear signal.
We use FrFT to filter out the noise which could not be removed by traditional FFT method.

## Slide 5: System Block Diagram
Host
Kernel
Kernel Function
(DFrFT)
Host Program
Read Signal Samples
Input File
Input Signal
Cutoff
Kernel Function
Domain
Signal
FilteredDomain Signal
Save to File
Result Signal
Output File

## Slide 6: Target Spec & Result Summary
Target Spec | 
Accuracy | Error less than 1%
Clock frequency | 200MHz
Area(Resource) | Be able to run on Zedboard
Latency | As low as possible
Result Summary | 
Accuracy | Error 1.06%
Timing Constraint | No negative slack
Area(Resource) | Highest Utilization 57% (BRAM)
Latency | 6ms ⟹ 0.3ms (reduce 95%)

## Slide 7: Fractional Fourier Transform (FrFT)
Definition:
Physical Meaning: Performing FT times
Effect on the time-frequency plane: Rotate the coordinates by angle

## Slide 8: Discrete Fractional Fourier Transform (DFrFT)
For hardware implementation, calculating exponential function (cordic) is time consuming, so we want to decompose the kernel function into function of and function of .
Convert the previous decomposition into discrete approximation, the kernel function would become a complex matrix
is the discrete form of Hermite-Gaussian Function

## Slide 9: Decompose The Kernel Function
For hardware implementation, calculating exponential function (cordic) is time consuming, so we want to decompose the kernel function into function of and function of .
Where is the k-th Hermite-Gaussian function, which is the eigenfunction of (Fractional) Fourier Transform

## Slide 10: Discrete Fractional Fourier Transform (DFrFT)
Convert the previous decomposition into discrete approximation, the kernel function would become a complex matrix
is the discrete form of Hermite-Gaussian Function
It’s hard to calculate Hermite-Gaussian Function either by hand or by computer. Further more, sampling could cause distortion

## Slide 11: Obtaining The Discrete Form of Hermite-Gaussian Function
We use the properties of the Hermite-Gaussian Function to obtain its discrete form.
Property 1: eigenfunction of Fourier Transform
Property 2: definition for Hermite-Gaussian Function
The discrete form of Hermite-Gaussian Function should be the eigenvector of the DFT matrix and the matrix representation, , of
=

## Slide 12: DFrFT Algorithm
Where is the matrix whose columns are the discrete Hermite-Gaussian functions
is the diagonal matrix with as diagonal terms

## Slide 13: Algorithm Simulation - DFrFT with different rotation angles

## Slide 14: Algorithm Simulation – Denoise by using DFrFT
Chirp is our signal.
Denoise

## Slide 15: Code Flow
Map to
Hermite-Gaussian Domain
Phase Shift
Map to
tα Domain
Twiddle Factor
Input f & Rotation angle α
Rotated input f

## Slide 16: HLS Optimization (1)
Use bundle for AXI-Master
Real, Imag
Real
Imag
Chart: latency(ns)
| bundle | baseline
latency(ns) | 3.343 | 5.96

## Slide 17: HLS Optimization (2)
Change the method of calculating matrix multiplication and use unroll 8.
Chart: latency(ms)
| unroll 8 | bundle
latency(ns) | 0.804 | 3.343

## Slide 18: HLS Optimization (3)
Map to
Hermite-Gaussian Domain
Twiddle Factor
Phase Shift
Map to
tα Domain
Input f
Rotation angle α
Rotated input f
Chart: latency(ms)
| dataflow + unroll4 | unroll 8
latency(ns) | 0.622 | 0.804
Use dataflow for parallel computing of “map to Hermite-Gaussian Domain” and “Twiddle Factor”

## Slide 19: HLS Optimization (4)
Chart: latency(ms)
| Final | dataflow + unroll4
latency(ns) | 0.346 | 0.622
Twiddle Factor

## Slide 20: HLS Optimization - Summary
Improvement

## Slide 21: Bring up PYNQ System (1)

## Slide 22: Bring up PYNQ System (2)
Algorithm Simulation
Implementation Result

## Slide 23: Conclusion
The filtered result has similar (or even better) performance as software simulation.
The latency of the 256-point DFrFT kernel is 0.3ms; on the other hand, sample rate of audio signals is usually 44100Hz.
Which means the DFrFT kernel as well as the filtering function could reach real-time performance.

## Slide 24: Thanks for listening!!!